## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #11
The Processor: Datapath

## Slide 2: Lecture #11a: Processor: Datapath
The Complete Datapath!
Brief Recap
From C to Execution
  3.1 Writing C Program
  3.2 Compiling to MIPS
  3.3 Assembling to Binaries
  3.4 Execution (Datapath)

## Slide 3
Complete Datapath
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
Left Shift 2-bit
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX

## Slide 4
2. Brief Recap
Lecture #7, Slide 4
Write program in high-level language (e.g., C)
if(x != 0) { a[0] = a[1] + x;
}

## Slide 5
2. Brief Recap
Lecture #7, Slide 4
Compiler translates to assembly language (e.g., MIPS)
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Else:

## Slide 6
2. Brief Recap
Lecture #7, Slide 4
Assembler translates to machine code (i.e., binaries)
0001 0010 0000 0000
0000 0000 0000 0011
1000 1110 0010 1000
0000 0000 0000 0100
0000 0010 0000 1000
0100 0000 0001 0100
1010 1110 0010 1000
0000 0000 0000 0000

## Slide 7
2. Brief Recap
Lecture #7, Slide 4
Processor executes the machine code (i.e., binaries)
Register
File
5
RegWrite
ALU
ALUcontrol
MemWrite
PC
4
PCSrc
Instruction
Memory
RegDst
MemRead
ALUSrc
MemToReg
5
5
Data
Memory

## Slide 8
3. From C to Execution
We play the role of Programmer, Compiler, Assembler, and Processor
  Program:
if(x != 0) { a[0] = a[1] + x; }
  Programmer:
    Show the workflow of compiling, assembling, and executing C program
  Compiler:
    Show how the program is compiled into MIPS
  Assembler:
    Show how the MIPS is translated into binaries
  Processor:
    Show how the datapath is activated in the processor

## Slide 9
3.1 Writing C Program
Edit, Compile, Execute: Lecture #2, Slide 5
Compile
Execute
Edit
produces
Source code
Edit
eg: vim recap.c
produces
Executable code
a.out
Compile
eg: gcc recap.c
produces
Execute
eg: a.out
No output expected
Program output
Incorrect result?
Cannot compile?
recap.c
if(x != 0) { a[0] =
a[1] + x;
}

## Slide 10
3.2 Compiling to MIPS
Key Idea #1: Compilation is a structured process
  if(x != 0) { a[0] = a[1] + x; }
  Each structure can be compiled independently
recap.c
if(x != 0) { a[0] =
a[1] + x;
}
if(x != 0) {
}
a[0] = a[1] + x;
Outer Structure
Inner Structure

## Slide 11
3.2 Compiling to MIPS
Key Idea #2: Variable-to-Register Mapping
  if(x != 0) { a[0] = a[1] + x; }
  Let the mapping be:
recap.c
if(x != 0) { a[0] =
a[1] + x;
}
Variable | Register Name | Register Number
x | $s0 | $16
a | $s1 | $17

## Slide 12
3.2 Compiling to MIPS
Common Technique #1: Invert the condition for shorter code (Lecture #8, Slide 22)
recap.c
if(x != 0) { a[0] =
a[1] + x;
}
if(x != 0) {
}
Outer Structure
beq $16, $0, Else
# Inner Structure
Else:
Outer MIPS Code
Mapping:
x: $16
a: $17

## Slide 13
3.2 Compiling to MIPS
Common Technique #2: Break complex operations, use temp register (Lecture #7, Slide 29)
recap.c
if(x != 0) { a[0] =
a[1] + x;
}
Mapping:
x: $16
a: $17
$t1: $8
a[0] = a[1] + x;
Inner Structure
$t1 = a[1];
$t1 = $t1 + x;
a[0] = $t1;
Simplified Inner Structure

## Slide 14
3.2 Compiling to MIPS
Common Technique #3: Array access is lw, array update is sw (Lecture #8, Slide 13)
recap.c
if(x != 0) { a[0] =
a[1] + x;
}
Mapping:
x: $16
a: $17
$t1: $8
$t1 = a[1];
$t1 = $t1 + x;
a[0] = $t1;
Simplified Inner Structure
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Inner MIPS Code

## Slide 15
3.2 Compiling to MIPS
Common Error #1: Assume that the address of the next word can be found by incrementing the address in a register by 1 instead of by the word size in bytes
  Example:
    $t1 = a[1]; is translated to lw $8, 4($17) instead of lw $8, 1($17)
recap.c
if(x != 0) { a[0] =
a[1] + x;
}
Mapping:
x: $16
a: $17
$t1: $8

## Slide 16
3.2 Compiling to MIPS
Last Step: Combine the two structures logically
recap.c
if(x != 0) { a[0] =
a[1] + x;
}
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Inner MIPS Code
Mapping:
x: $16
a: $17
$t1: $8
beq $16, $0, Else
# Inner Structure
Else:
Outer MIPS Code
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
  sw $8, 0($17)
Else:
Combined MIPS Code

## Slide 17
3.3 Assembling to Binary
Instruction Types Used:
  R-Format: (Lecture #9, Slide 8)
    opcode $rd, $rs, $rt
  I-Format: (Lecture #9, Slide 14)
    opcode $rt, $rs, immediate
  Branch: (Lecture #9, Slide 22)
    Uses I-Format
    PC = (PC + 4) + (immediate  4)
opcode
rs
rt
rd
shamt
funct
6
5
5
5
6
5
opcode
rs
rt
immediate
6
5
5
16
recap.mips
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Else:

## Slide 18
3.3 Assembling to Binary
beq $16, $0, Else
  Compute immediate value (Lecture #9, Slide 27)
    immediate = 3
  Fill in fields (refer to MIPS Reference Data)
  Convert to binary
recap.mips
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Else:
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
  sw $8, 0($17)
Else:
4
16
0
3
6
5
5
16
000100
10000
00000
0000000000000011
+3

## Slide 19
3.3 Assembling to Binary
lw $8, 4($17)
  Fill in fields (refer to MIPS Reference Data)
  Convert to binary
recap.mips
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Else:
0001 0010 0000 0000 0000 0000 0000 0011
lw $8, 4($17) add $8, $8, $16
  sw $8, 0($17)
Else:
35
17
8
4
6
5
5
16
100011
10001
01000
0000000000000100

## Slide 20
3.3 Assembling to Binary
add $8, $8, $16
  Fill in fields (refer to MIPS Reference Data)
  Convert to binary
recap.mips
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Else:
0001 0010 0000 0000 0000 0000 0000 0011
1000 1110 0010 1000 0000 0000 0000 0100 add $8, $8, $16
  sw $8, 0($17)
Else:
0
8
16
8
0
32
6
5
5
5
6
5
000000
01000
10000
01000
00000
100000

## Slide 21
3.3 Assembling to Binary
sw $8, 0($17)
  Fill in fields (refer to MIPS Reference Data)
  Convert to binary
recap.mips
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Else:
0001 0010 0000 0000 0000 0000 0000 0011
1000 1110 0010 1000 0000 0000 0000 0100 0000 0001 0001 0000 0100 0000 0010 0000
sw $8, 0($17)
Else:
43
17
8
0
6
5
5
16
101011
10001
01000
0000000000000000

## Slide 22
3.3 Assembling to Binary
Final Binary
  Hard to read?
  Don’t worry, this is intended for machine not for human!
recap.mips
beq $16, $0, Else
lw $8, 4($17) add $8, $8, $16
sw $8, 0($17)
Else:
0001 0010 0000 0000 0000 0000 0000 0011
1000 1110 0010 1000 0000 0000 0000 0100 0000 0001 0001 0000 0100 0000 0010 0000
1010 1110 0010 1000 0000 0000 0000 0000

## Slide 23
3.4 Execution (Datapath)
Given the binary
  Assume two possible executions:
    $16 == $0 (shorter)
    $16 != $0 (longer )
  Convention:
    Fetch: Memory:
    Decode: Reg Write:
    ALU: Other:
0001 0010 0000 0000 0000 0000 0000 0011
1000 1110 0010 1000 0000 0000 0000 0100 0000 0001 0001 0000 0100 0000 0010 0000
1010 1110 0010 1000 0000 0000 0000 0000

## Slide 24
beq $16, $0, Else
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
opcode
31:26
rs
25:21
rt
20:16
immediate
10:6
000100
10000
0000
0000000000000011
Left Shift 2-bit
Assume $16 == $0
$16
$0
R[$16]
R[$0]
TRUE

## Slide 25
beq $16, $0, Else
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
opcode
31:26
rs
25:21
rt
20:16
immediate
10:6
000100
10000
0000
0000000000000011
Left Shift 2-bit
Assume $16 != $0
$16
$0
R[$16]
R[$0]
FALSE

## Slide 26
lw $8, 4($17)
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
5
5
5
RegWrite
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
opcode
31:26
rs
25:21
rt
20:16
immediate
10:6
100011
10001
01000
Left Shift 2-bit
Assume $16 != $0
0000000000000100
Sign Extend
$17
$8
R[$17]
4
R[$17]+4
M[R[$17]+4]
M[R[$17]+4]

## Slide 27
add $8, $8, $16
Inst [25:21]
Inst [20:16]
MUX
Inst [15:0]
MUX
5
5
5
RegWrite
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
Left Shift 2-bit
Assume $16 != $0
Sign Extend
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01000
10000
01000
00000
100000
Inst [15:11]
$8
$16
$8
R[$18]
R[$16]
R[$18]+R[$16]

## Slide 28
sw $8, 0($17)
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
5
5
5
RegWrite
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
opcode
31:26
rs
25:21
rt
20:16
immediate
10:6
101011
10001
01000
Left Shift 2-bit
Assume $16 != $0
0000000000000000
Sign Extend

## Slide 29: End of File