## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #12
The Processor: Control

## Slide 2: Lecture #12: Processor: Control
Identified Control Signals
Generating Control Signals: Idea
The Control Unit
Control Signals
ALU Control Signal
Instruction Execution

## Slide 3
Complete Datapath
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
Left Shift 2-bit
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX

## Slide 4
1. Identified Control Signals
Control Signal | Execution Stage | Purpose
RegDst | Decode/Operand Fetch | Select the destination register number
RegWrite | Decode/Operand Fetch RegWrite | Enable writing of register
ALUSrc | ALU | Select the 2nd operand for ALU
ALUControl | ALU | Select the operation to be performed
MemRead / MemWrite | Memory | Enable reading/writing of data memory
MemToReg | RegWrite | Select the result to be written back to register file
PCSrc | Memory/RegWrite | Select the next PC value

## Slide 5
2. Generating Control Signals: Idea
The control signals are generated based on the instruction to be executed:
  Opcode  Instruction Format
  Example:
    R-Format instruction  RegDst = 1 (use Inst[15:11]) )
  R-Type instruction has additional information:
    The 6-bit "funct" (function code, Inst[5:0]) field
Idea:
  Design a combinatorial circuit to generate these signals based on Opcode and possibly Function code
    A control unit is needed (a draft design is shown next)

## Slide 6
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
Left Shift 2-bit
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX
Control
The Control Unit (draft)

## Slide 7
3. Let’s Implement the Control Unit!
Approach:
  Take note of the instruction subset to be implemented:
    Opcode and Function Code (if applicable)
  Go through each signal:
    Observe how the signal is generated based on the instruction opcode and/or function code
  Construct truth table
  Design the control unit using logic gates

## Slide 8
3. MIPS Instruction Subset (Review)
016
rs
rt
rd
0
2016
016
2216
016
2416
016
2516
016
2A16
add
sub
and
or
slt
opcode
shamt
funct
R-type
31
25
20
15
10
5
2316
offset
2B16
416
lw
sw
beq
I-type
31
25
20
15
rs
rt
rd
0
rs
rt
rd
0
rs
rt
rd
0
rs
rt
rd
0
rs
rd
offset
rs
rd
offset
rs
rd

## Slide 9
4. Control Signal: RegDst
False (0): Write register = Inst[20:16]
True (1): Write register = Inst[15:11]
MUX
0
1
Signal

## Slide 10
4. Control Signal: RegWrite
False (0): No register write
True (1): New value will be written

## Slide 11
4. Control Signal: ALUSrc
False (0): Operand2 = Register Read Data 2
True (1): Operand2 = SignExt(Inst[15:0])

## Slide 12
4. Control Signal: MemRead
False (0): Not performing memory read access
True (1): Read memory using Address

## Slide 13
4. Control Signal: MemWrite
False (0): Not performing memory write operation
True (1): memory[Address]  Register Read Data 2

## Slide 14
4. Control Signal: MemToReg
True (1): Register write data = Memory read data
False (0): Register write data = ALU result
MUX
1
0
Signal
IMPORTANT:
The input of MUX is swapped in this case

## Slide 15
4. Control Signal: PCSrc (1/2)
The "isZero?" signal from the ALU gives us the actual branch outcome (taken/not taken)
Idea: “If instruction is a branch AND taken, then…”

## Slide 16
4. Control Signal: PCSrc (2/2)
False (0): Next PC = PC + 4
True (1): Next PC = SignExt(Inst[15:0]) << 2 + (PC + 4)
PCSrc =
( Branch AND isZero)

## Slide 17
4. Midpoint Check
Control Signal | Execution Stage | Purpose
RegDst | Decode/Operand Fetch | Select the destination register number
RegWrite | Decode/Operand Fetch RegWrite | Enable writing of register
ALUSrc | ALU | Select the 2nd operand for ALU
ALUControl | ALU | Select the operation to be performed
MemRead / MemWrite | Memory | Enable reading/writing of data memory
MemToReg | RegWrite | Select the result to be written back to register file
PCSrc | Memory/RegWrite | Select the next PC value
We have gone through almost all of the signals:
  Left with the more challenging ALUControl signal
Observation so far:
  The signals discussed so far can be generated by opcode directly
    Function code is not needed up to this point
  A major part of the controller can be built based on opcode alone

## Slide 18
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Registers
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
4
Data
Memory
Address
Read
Data
Write
Data
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
Left Shift 2-bit
PC
Add
4
Add
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
MUX
Control
PCSrc
MUX
Branch
ALUcontrol
Inst [31:26]
MemToReg
MemWrite
ALUSrc
The Control Unit v0.5

## Slide 19
5. Closer Look at ALU
The ALU is a combinatorial circuit:
  Capable of performing several arithmetic operations
In Lecture #11:
  We noted the required operations for the MIPS subset
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
Question:
  How is the ALUcontrol signal designed?

## Slide 20
5. One Bit At A Time
A simplified 1-bit MIPS ALU can be implemented as follows:
4 control bits are needed:
  Ainvert:
    1 to invert input A
  Binvert:
    1 to invert input B
  Operation (2-bit)
    To select one of the 3 results
Acknowledgement: Image taken from NYU Course CSCI-UA.0436

## Slide 21
5. One Bit At A Time (Aha!)
Can you see how the ALUcontrol (4-bit) signal controls the ALU?
  Note: implementation for slt not shown
Acknowledgement: Image taken from NYU Course CSCI-UA.0436
ALUcontrol |  |  | Function
Ainvert | Binvert | Operation | 
0 | 0 | 00 | AND
0 | 0 | 01 | OR
0 | 0 | 10 | add
0 | 1 | 10 | subtract
0 | 1 | 11 | slt
1 | 1 | 00 | NOR

## Slide 22
5. Multilevel Decoding
Now we can start to design for ALUcontrol signal, which depends on:
  Opcode (6-bit) field and Function Code (6-bit) field
Brute Force approach:
  Use Opcode and Function Code directly, i.e. finding expressions with 12 variables
Multilevel Decoding approach:
  Use some of the input to reduce the cases, then generate the full output
  Simplify the design process, reduce the size of the main controller, potentially speedup the circuit

## Slide 23
5. Intermediate Signal: ALUop
Basic Idea:
  Use Opcode to generate a 2-bit ALUop signal
    Represents classification of the instructions:
  Use ALUop signal and Function Code field (for R-type instructions) to generate the 4-bit ALUcontrol signal
Instruction type | ALUop
lw / sw | 00
beq | 01
R-type | 10

## Slide 24
5. Two-level Implementation
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
6
Control
ALU Control
6
ALU
4
ALUcontrol
ALUop
2
00: lw, sw
01: beq
10: add, sub, and, or, slt
0000: and
0001: or
0010: add
0110: sub
0111: set on less than
Step 1.
Generate 2-bit ALUop signal from 6-bit opcode.
Step 2.
Generate ALUcontrol signal from ALUop and optionally 6-bit Funct field.

## Slide 25
5. Generating ALUcontrol Signal

Opcode | ALUop | Instruction Operation | Funct field | ALU action | ALU control
lw |  | load word |  | add | 
sw |  | store word |  | add | 
beq |  | branch equal |  | subtract | 
R-type |  | add |  | add | 
R-type |  | subtract |  | subtract | 
R-type |  | AND |  | AND | 
R-type |  | OR |  | OR | 
R-type |  | set on less than |  | set on less than | 
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
Generation of 2-bit ALUop signal will be discussed later
00
00
01
10
10
10
10
10
xxxxxx
xxxxxx
xxxxxx
10 0000
10 0010
10 0101
10 0100
10 1010
0010
0010
0110
0010
0110
0001
0000
0111
Instruction Type | ALUop
lw / sw | 00
beq | 01
R-type | 10

## Slide 26
5. Design of ALU Control Unit (1/2)

Input: 6-bit Funct field and 2-bit ALUop
Output: 4-bit ALUcontrol
Find the simplified expressions
 | ALUop |  | Funct Field ( F[5:0] == Inst[5:0] ) |  |  |  |  |  | ALU control
 | MSB | LSB | F5 | F4 | F3 | F2 | F1 | F0 | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sub |  |  |  |  |  |  |  |  | 
and |  |  |  |  |  |  |  |  | 
or |  |  |  |  |  |  |  |  | 
slt |  |  |  |  |  |  |  |  | 
0
0
X
X
X
X
X
X
0 0 1 0
0
0
X
X
X
X
X
X
0 0 1 0
0
1
X
X
X
X
X
X
0 1 1 0
X
1
0
1
0
0
0
0
0
0 0 1 0
1
0
1
0
0
0
1
0
0 1 1 0
1
0
1
0
0
1
0
0
0 0 0 0
1
0
1
0
0
1
0
1
0 0 0 1
1
0
1
0
1
0
1
0
0 1 1 1
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
ALUcontrol3 = 0
ALUcontrol2 = ?
ALUop0 + ALUop1 F1

## Slide 27
5. Design of ALU Control Unit (2/2)
Simple combinational logic
ALUcontrol2
= ALUOp0 + ALUOp1∙F1
ALUcontrol
ALUcontrol3
0
ALUcontrol2
ALUcontrol1
ALUcontrol0
ALU Control block
ALUop
ALUOp0 (LSB)
ALUOp1 (MSB)
F3
F2
F1
F0
F(5-0)
2

## Slide 28
5. Finale: Control Design
We have now considered all individual signals and their expected values
  Ready to design the controller itself
Typical digital design steps:
  Fill in truth table
    Input: Opcode
    Output: Various control signals as discussed
  Derive simplified expression for each signal

## Slide 29
ALU Control
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Registers
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
4
Data
Memory
Address
Read
Data
Write
Data
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
Left Shift 2-bit
PC
Add
4
Add
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
MUX
Control
PCSrc
MUX
Branch
ALUcontrol
Inst [31:26]
Inst [5:0]
ALUop
MemToReg
MemWrite
ALUSrc
Datapath & Control

## Slide 30
5. Control Design: Outputs

 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
0
0
1
1
0
0
0
1
0
1
1
0
1
0
1
0
0
0
1
X
X
0
1
0
0
0
0
0
X
X
0
0
0
1
0
1

## Slide 31
5. Control Design: Inputs
With the input (opcode) and output (control signals), let’s design the circuit
 | Opcode ( Op[5:0] == Inst[31:26] ) |  |  |  |  |  | 
 | Op5 | Op4 | Op3 | Op2 | Op1 | Op0 | Value in Hexadecimal
R-type |  |  |  |  |  |  | 
lw |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | 
beq |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
1
0
1
1
23
0
1
1
0
1
1
2B
0
0
0
1
0
0
4

## Slide 32
5. Combinational Circuit Implementation
Opcode
Control Signals
 | Opcode |  |  |  |  | 
 | Op5 | Op4 | Op3 | Op2 | Op1 | Op0
R-type | 0 | 0 | 0 | 0 | 0 | 0
lw | 1 | 0 | 0 | 0 | 1 | 1
sw | 1 | 0 | 1 | 0 | 1 | 1
beq | 0 | 0 | 0 | 1 | 0 | 0

## Slide 33
5. Combinational Circuit Implementation
 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0
beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1
Opcode
Control Signals

## Slide 34
6. Big Picture: Instruction Execution
Instruction Execution =
  Read contents of one or more storage elements (register/memory)
  Perform computation through some combinational logic
  Write results to one or more storage elements (register/memory)
All these performed within a clock period
Clock
Clock Period
Read
Compute
Write
Don’t want to read a storage element when it is being written.

## Slide 35
6. Single Cycle Implementation: Shortcoming
Calculate cycle time assuming negligible delays: memory (2ns), ALU/adders (2ns), register file access (1ns)
Instruction | Inst Mem | Reg read | ALU | Data Mem | Reg write | Total
ALU | 2 | 1 | 2 |  | 1 | 6
lw | 2 | 1 | 2 | 2 | 1 | 8
sw | 2 | 1 | 2 | 2 |  | 7
beq | 2 | 1 | 2 |  |  | 5
All instructions take as much time as the slowest one (i.e., load)
 Long cycle time for each instruction

## Slide 36
6. Solution #1: Multicycle Implementation
Break up the instructions into execution steps:
  Instruction fetch
  Instruction decode and register read
  ALU operation
  Memory read/write
  Register write
Each execution step takes one clock cycle
   Cycle time is much shorter, i.e., clock frequency is much higher
Instructions take variable number of clock cycles to complete execution
Not covered in class:
  See Section 5.5 of COD if interested

## Slide 37
6. Solution #2: Pipelining
Break up the instructions into execution steps one per clock cycle
Allow different instructions to be in different execution steps simultaneously
Covered in a later lecture

## Slide 38
Summary
A very simple implementation of MIPS datapath and control for a subset of its instructions
Concepts:
  An instruction executes in a single clock cycle
  Read storage elements, compute, write to storage elements
  Datapath is shared among different instructions types using MUXs and control signals
  Control signals are generated from the machine language encoding of instructions

## Slide 39
Reading
The Processor: Datapath and Control
  COD Chapter 5 Sections 5.4 (3rd edition)
  COD Chapter 4 Sections 4.4 (4th edition)
Exploration:
  ALU design and implementation:
    4th edition (MIPS): Appendix C
    http://cs.nyu.edu/courses/fall11/CSCI-UA.0436-001/class-notes.html

## Slide 40: End of File