## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #6
C for Hardware Programming

## Slide 2: Lecture #6: C for Hardware Programming
Overview and Motivation
Hardware Programming: Concerns
C and Hardware Programming
Code Compilation Process
Debugging – GDB

## Slide 3
1. Overview and Motivation
  C is a high-level language which is widely used to program microcontrollers and single board computers
  Capability to address hardware memory locations
  Capability to address hardware enhancements by the vendor
  Another extension of the C language to support certain exclusive features required in embedded systems is Embedded C
  Here, we briefly introduce C based hardware programming and not embedded C

## Slide 4
2. Hardware Programming: Concerns
Code speed
  Timing constraints
  Slow processor compared to desktop processors
Code size
  Limited memory
Programming methods
Machine code (0,1)
High difficulty
Almost no readability
Assembly language (ADD, SLL, etc.)
Low readability
Difficult in large projects
C
Fairly efficient
High readability
High speed, low size
Suitable for large projects

## Slide 5
3. C and Hardware Programming
  Gives symbolic names to values
  Provides abstraction of underlying hardware
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!

## Slide 6
4. Code Compilation Process (1/8)
Preprocessing: It is the first stage of compilation. It processes preprocessor directives like include-files, conditional compilation instructions and macros.
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!
file1.i
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 7
4. Code Compilation Process (2/8)
Preprocessing: It is the first stage of compilation. It processes preprocessor directives like include-files, conditional compilation instructions and macros.
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!
file1.i
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 8
4. Code Compilation Process (3/8)
Preprocessing: It is the first stage of compilation. It processes preprocessor directives like include-files, conditional compilation instructions and macros.
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!
file1.i
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 9
4. Code Compilation Process (4/8)
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!
Compilation: It is the second stage. It takes the output of the preprocessor with the source code, and generates assembly source code.
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 10
4. Code Compilation Process (5/8)
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!
Assembler stage: It is the third stage of compilation. It takes the assembly source code and produces the corresponding object code.
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 11
4. Code Compilation Process (6/8)
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!
Linking: It is the final stage of compilation. It takes one or more object files or libraries and linker script as input and combines them to produce a single executable file.
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 12
4. Code Compilation Process (7/8)
Code Compilation Process
C Program (.c)
Preprocessor
Preprocessed code (.i)
Compiler
Assembly code (.asm)
Linker
External libs., etc.
Executable (.hex)
Assembler
Object code (.o)
Burn program to hardware and run!
In doing so, it resolves references to external symbols, assigns final addresses to procedures/functions and variables, and revises code and data to reflect new addresses (a process called relocation).
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 13
4. Code Compilation Process (8/8)
Notes: https://www.slideshare.net/mohabdallah/embedded-c-lecture-1

## Slide 14
5. Debugging – GDB (1/6)
GDB or GNU Debugger is used to debug C programs
It is used to inspect, step by step, the execution of a program
Commands:
  Start
  Step
  explore
  print <variable>
  run
  Continue
  up
  down
  where
Notes: - https://www.youtube.com/watch?v=xQ0ONbt-qPs
- https://www.youtube.com/watch?v=rlN3XI8kuhI

## Slide 15
5. Debugging – GDB (2/6)
Notes: - https://www.youtube.com/watch?v=xQ0ONbt-qPs
- https://www.youtube.com/watch?v=rlN3XI8kuhI

## Slide 16
5. Debugging – Sample (3/6)
Program to print the days of the week:
#include <stdio.h>
int main(void) {
int i;
char *day[7] = {
"Monday",
"Tuesday",
"Wednesday",
"Thursday",
"Friday",
"Saturday",
"Sunday"
};
for (i = 0; i<=10; i++) {
printf("Day[%d] = %s \n", i, day[i]);
}
return 0;
}
Notes: - https://www.youtube.com/watch?v=xQ0ONbt-qPs
- https://www.youtube.com/watch?v=rlN3XI8kuhI

## Slide 17
5. Debugging – Sample (4/6)
GDB
Step: helps iterating through the program step by step
Print: gives you the current value of the variable
List: lists the program
To change parameters
Notes: - https://www.youtube.com/watch?v=xQ0ONbt-qPs
https://www.youtube.com/watch?v=rlN3XI8kuhI
https://sourceware.org/bugzilla/show_bug.cgi?id=20981

## Slide 18
5. Debugging – Sample (5/6)
Segmentation fault
Notes: - https://www.youtube.com/watch?v=xQ0ONbt-qPs
https://www.youtube.com/watch?v=rlN3XI8kuhI
https://sourceware.org/bugzilla/show_bug.cgi?id=20981

## Slide 19
5. Debugging – Sample (6/6)
Program to print the days of the week:
#include <stdio.h>
int main(void) {
int i;
char *day[7] = {
"Monday",
"Tuesday",
"Wednesday",
"Thursday",
"Friday",
"Saturday",
"Sunday"
};
for (i = 0; i<=10; i++) {
printf("Day[%d] = %s \n", i, day[i]);
}
return 0;
}
Line 11
Notes: - https://www.youtube.com/watch?v=xQ0ONbt-qPs
https://www.youtube.com/watch?v=rlN3XI8kuhI
https://sourceware.org/bugzilla/show_bug.cgi?id=20981

## Slide 20: End of File