## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #9
MIPS
Part III: Instruction Formats and Encoding

## Slide 2: Lecture #9: MIPS Part 3: Instruction Formats
Overview and Motivation
MIPS Encoding: Basics
MIPS Instruction Classification
MIPS Registers (Recap)
R-Format
  5.1 R-Format: Example
  5.2 Try It Yourself #1

## Slide 3: Lecture #9: MIPS Part 3: Instruction Formats
I-Format
  6.1 I-Format: Example
  6.2 Try It Yourself #2
  6.3 Instruction Address: Overview
  6.4 Branch: PC-Relative Addressing
  6.5 Branch: Example
  6.6 Try It Yourself #3
J-Format
  7.1 J-Format: Example9
  7.2 Branching Far Away: Challenge
Addressing Modes

## Slide 4
1. Overview and Motivation
Recap: Assembly instructions will be translated to machine code for actual execution
  This section shows how to translate MIPS assembly code into binary patterns
Explains some of the “strange facts” from earlier:
  Why is immediate limited to 16 bits?
  Why is shift amount only 5 bits?
  etc.
Prepare us to “build” a MIPS processor in later lectures!

## Slide 5
2. MIPS Encoding: Basics
Each MIPS instruction has a fixed-length of 32 bits
   All relevant information for an operation must be encoded with these bits!
Additional challenge:
  To reduce the complexity of processor design, the instruction encodings should be as regular as possible
   Small number of formats, i.e. as few variations as possible

## Slide 6
3. MIPS Instruction Classification
Instructions are classified according to their operands:
   Instructions with same operand types have same encoding
R-format (Register format: op $r1, $r2, $r3)
Instructions which use 2 source registers and 1 destination register
e.g. add, sub, and, or, nor, slt, etc
I-format (Immediate format: op $r1, $r2, Immd)
e.g. addi, andi, ori, slti, lw, sw, beq, bne, etc.
J-format (Jump format: op Immd)
j instruction uses only one immediate value
Instructions which use 1 source register, 1 immediate value and 1 destination register
Special cases: srl, sll, etc.

## Slide 7
4. MIPS Registers (Recap)
For simplicity, register numbers ($0, $1, …, $31) will be used in examples here instead of register names
Name | Register number | Usage
$zero | 0 | Constant value 0
$v0-$v1 | 2-3 | Values for results and expression evaluation
$a0-$a3 | 4-7 | Arguments
$t0-$t7 | 8-15 | Temporaries
$s0-$s7 | 16-23 | Program variables
Name | Register number | Usage
$t8-$t9 | 24-25 | More temporaries
$gp | 28 | Global pointer
$sp | 29 | Stack pointer
$fp | 30 | Frame pointer
$ra | 31 | Return address
$at (register 1) is reserved for the assembler.
$k0-$k1 (registers 26-27) are reserved for the operation system.

## Slide 8
5. R-Format (1/2)
Define fields with the following number of bits each:
  6 + 5 + 5 + 5 + 5 + 6 = 32 bits
6
5
5
5
6
5
Each field has a name:
Each field is an independent 5- or 6-bit unsigned integer
  A 5-bit field can represent any number 0 – 31
  A 6-bit field can represent any number 0 – 63
opcode
rs
rt
rd
shamt
funct

## Slide 9
5. R-Format (2/2)
Fields | Meaning
opcode | - Partially specifies the instruction - Equal to 0 for all R-Format instructions
funct | - Combined with opcode exactly specifies the instruction
rs (Source Register) | - Specify register containing first operand
rt (Target Register) | - Specify register containing second operand
rd (Destination Register) | - Specify register which will receive result of computation
shamt | Amount a shift instruction will shift by 5 bits (i.e. 0 to 31) - Set to 0 in all non-shift instructions

## Slide 10
5.1 R-Format: Example (1/3)
add $8, $9, $10
MIPS instruction
R-Format Fields | Value | Remarks
opcode | 0 | (textbook pg 94 - 101)
funct | 32 | (textbook pg 94 - 101)
rd | 8 | (destination register)
rs | 9 | (first operand)
rt | 10 | (second operand)
shamt | 0 | (not a shift instruction)

## Slide 11
5.1 R-Format: Example (2/3)
Field representation in decimal:
0
9
10
8
32
0
opcode
rs
rt
rd
shamt
funct
Field representation in binary:
Note the ordering of the 3 registers
000000
01001
01010
01000
00000
100000
0000
0001
0010
1010
0100
0000
0010
0000
Split into 4-bit groups for hexadecimal conversion:
016
116
216
A16
416
016
216
016
add $8, $9, $10
MIPS instruction

## Slide 12
5.1 R-Format: Example (3/3)
Field representation in decimal:
0
0
9
8
0
4
opcode
rs
rt
rd
shamt
funct
Field representation in binary:
000000
00000
01001
01000
00100
000000
0000
0000
0000
1001
0100
0001
0000
0000
Split into 4-bit groups for hexadecimal conversion:
016
016
016
916
416
116
016
016
Note the placement of the source register
sll $8, $9, 4
MIPS instruction

## Slide 13
5.2 Try It Yourself #1
Field representation in decimal:
opcode
rs
rt
rd
shamt
funct
Field representation in binary:
Hexadecimal representation of instruction:

add $10, $7, $5
MIPS instruction
0
7
5
10
0
32
000000
00111
00101
01010
00000
100000
0 0 E 5 5 0 2 016

## Slide 14
6. I-format (1/4)
What about instructions with immediate values?
  5-bit shamt field can only represent 0 to 31
  Immediates may be much larger than this
    e.g. lw, sw instructions require bigger offset
Compromise: Define a new instruction format partially consistent with R-format:
  If instruction has immediate, then it uses at most 2 registers

## Slide 15
6. I-format (2/4)
Define fields with the following number of bits each:
  6 + 5 + 5 + 16 = 32 bits
Again, each field has a name:
Only one field is inconsistent with R-format.
  opcode, rs, and rt are still in the same locations.
6
5
5
16
opcode
rs
rt
immediate

## Slide 16
6. I-format (3/4)
opcode
  Since there is no funct field, opcode uniquely specifies an instruction
rs
  specifies the source register operand (if any)
rt
  specifies register to receive result
  note the difference from R-format instructions
Continue on next slide……

## Slide 17
6. I-format (4/4)
immediate:
  Treated as a signed integer
  16 bits  can be used to represent a constant up to 216 different values
  Large enough to handle:
    The offset in a typical lw or sw
    Most of the values used in the addi,subi, slti instructions

## Slide 18
6.1 I-format: Example (1/2)
addi $21, $22, -50
MIPS instruction
I-Format Fields | Value | Remarks
opcode | 8 | (textbook pg 94 - 101)
rs | 22 | (the only source register)
rt | 21 | (target register)
immediate | -50 | (in base 10)

## Slide 19
6.1 I-format: Example (2/2)
Hexadecimal representation of instruction:
2 2 D 5 F F C E16
Field representation in decimal:
8
22
21
-50
Field representation in binary:
001000
10110
10101
1111111111001110
addi $21, $22, -50
MIPS instruction

## Slide 20
6.2 Try It Yourself #2
Hexadecimal representation of instruction:

Field representation in decimal:
opcode
rs
rt
immediate
Field representation in binary:
lw $9, 12($8)
MIPS instruction
35
8
9
12
100011
01000
01001
0000000000001100
8 D 0 9 0 0 0 C16

## Slide 21
6.3 Instruction Address: Overview
As instructions are stored in memory, they too have addresses
  Control flow instructions uses these addresses
  E.g. beq, bne, j
As instructions are 32-bit long, instruction addresses are word-aligned as well
Program Counter (PC)
  A special register that keeps address of instruction being executed in the processor

## Slide 22
6.4 Branch: PC-Relative Addressing (1/5)
Use I-Format
opcode specifies beq, bne
rs and rt specify registers to compare
What can immediate specify?
  Immediate is only 16 bits
  Memory address is 32 bits
   immediate is not enough to specify the entire target address!
opcode
rs
rt
immediate

## Slide 23
6.4 Branch: PC-Relative Addressing (2/5)
How do we usually use branches?
  Answer: if-else, while, for
  Loops are generally small:
    Typically up to 50 instructions
  Unconditional jumps are done using jump instructions (j), not the branches
Conclusion: A branch often changes PC by a small amount
beq $9, $8, End
PC
End
End: …………………

## Slide 24
6.4 Branch: PC-Relative Addressing (3/5)
Solution:
  Specify target address relative to the PC
Target address is generated as:
  PC + the 16-bit immediate field
  The immediate field is a signed two’s complement integer
 Can branch to ± 215 bytes from the PC:
  Should be enough to cover most loops
PC
End
+
End2
-
beq $9,$8,End
End: …………………
End2: …………………

## Slide 25
6.4 Branch: PC-Relative Addressing (4/5)
Can the branch target range be enlarged?
Observation: Instructions are word-aligned
  Number of bytes to add to the PC will always be a multiple of 4.
   Interpret the immediate as number of words, i.e. automatically multiplied by 410 (1002)
 Can branch to ± 215 words from the PC
  i.e. ± 217 bytes from the PC
  We can now branch 4 times farther!

## Slide 26
6.4 Branch: PC-Relative Addressing (5/5)
Branch calculation:
  Observations:
    immediate field specifies the number of words to jump, which is the same as the number of instructions to “skip over”
    immediate field can be positive or negative
    Due to hardware design, add immediate to (PC+4), not to PC (more in later topic)
  If the branch is not taken:
  PC = PC + 4
  (PC + 4 is address of next instruction)
  If the branch is taken:
  PC = (PC + 4) + (immediate  4)

## Slide 27
6.5 Branch: Example (1/3)
beq is an I-Format instruction 
I-Format Fields | Value | Remarks
opcode | 4 | 
rs | 9 | (first operand)
rt | 0 | (second operand)
immediate | ??? | (in base 10)
Loop: beq $9, $0, End # rlt addr: 0
add $8, $8, $10 # rlt addr: 4
addi $9, $9, -1 # rlt addr: 8
j Loop # rlt addr: 12
End: # rlt addr: 16

## Slide 28
6.5 Branch: Example (2/3)
Loop: beq $9, $0, End # rlt addr: 0
add $8, $8, $10 # rlt addr: 4
addi $9, $9, -1 # rlt addr: 8
j Loop # rlt addr: 12
End: # rlt addr: 16
immediate field:
  Number of instructions to add to (or subtract from) the PC, starting at the instruction following the branch
  In beq case, immediate = 3
  End = (PC + 4) + (immediate  4)

## Slide 29
6.5 Branch: Example (3/3)
Loop: beq $9, $0, End # rlt addr: 0
add $8, $8, $10 # rlt addr: 4
addi $9, $9, -1 # rlt addr: 8
j Loop # rlt addr: 12
End: # rlt addr: 16
Field representation in decimal:
opcode
rs
rt
immediate
4
9
0
3
Field representation in binary:
000100
01001
00000
0000000000000011

## Slide 30
6.6 Try It Yourself #3
What would be the immediate value for the second beq instruction?
Answer: – 4

Loop: beq $9, $0, End # rlt addr: 0
add $8, $8, $10 # rlt addr: 4
addi $9, $9, -1 # rlt addr: 8
beq $0, $0, Loop # rlt addr: 12
End: # rlt addr: 16

## Slide 31
7. J-Format (1/5)
For branches, PC-relative addressing was used:
  Because we do not need to branch too far
For general jumps (j):
  We may jump to anywhere in memory!
The ideal case is to specify a 32-bit memory address to jump to
  Unfortunately, we can’t ( why?)

## Slide 32
7. J-Format (2/5)
Define fields of the following number of bits each:
6 bits
26 bits
As usual, each field has a name:
opcode
target address
Keep opcode field identical to R-format and I-format for consistency
Combine all other fields to make room for larger target address

## Slide 33
7. J-Format (3/5)
We can only specify 26 bits of 32-bit address
Optimization:
  Just like with branches, jumps will only jump to word-aligned addresses, so last two bits are always 00
  So, let’s assume the address ends with ’00’ and leave them out
 Now we can specify 28 bits of 32-bit address

## Slide 34
7. J-Format (4/5)
Where do we get the other 4 bits?
  MIPS choose to take the 4 most significant bits from PC+4 (the next instruction after the jump instruction)
   This means that we cannot jump to anywhere in memory, but it should be sufficient most of the time
Question:
  What is the maximum jump range?
256MB boundary
Special instruction if the program straddles 256MB boundary
  Look up jr instruction if you are interested
  Target address is specified through a register

## Slide 35
7. J-Format (5/5)
Summary: Given a Jump instruction
opcode
target address
000010
00001111000011110000111100
32bit PC
1010………
Jumps To
1010
00001111000011110000111100
00
Most significant 4bits of PC+4
26bits Target address specified in instruction
Default 2bit "00" for word address

## Slide 36
7.1 J-Format: Example
  Loop: beq $9, $0, End # addr: 8
  add $8, $8, $10 # addr: 12
  addi $9, $9, -1 # addr: 16
  j Loop # addr: 20
  End: # addr: 24
0000………………………..01000
Address to jump to
immediate =2 (26 bits)
0000………………………..10100
PC
PC
Check your understanding by constructing the new PC value
opcode
target address
000010
00000000000000000000000010
jump target

## Slide 37
7.2 Branching Far Way
Given the instruction beq $s0, $s1, L1 Assume that the address L1 is farther away from the PC than can be supported by beq and bne instructions
Challenge:
  Construct an equivalent code sequence with the help of unconditional (j) and conditional branch (beq, bne) instructions to accomplish this far away branching

## Slide 38
8. Addressing Modes (1/3)
Register addressing: operand is a register
op
rs
rt
rd
funct
Register
Immediate addressing: operand is a constant within the instruction itself (addi, andi, ori, slti)
op
rs
rt
immediate

## Slide 39
8. Addressing Modes (2/3)
Base addressing (displacement addressing): operand is at the memory location whose address is sum of a register and a constant in the instruction (lw, sw)
op
rs
rt
Address
Register
+
Memory
word

## Slide 40
8. Addressing Modes (3/3)
PC-relative addressing: address is sum of PC and constant in the instruction (beq, bne)
op
rs
rt
Address
PC
+
Memory
word
Pseudo-direct addressing: 26-bit of instruction concatenated with upper 4-bits of PC (j)
op
Address
PC
:
Memory
word

## Slide 41
Summary (1/2)
MIPS Instruction: 32 bits representing a single instruction
opcode
rs
rt
immediate
opcode
rs
rt
rd
funct
shamt
R
I
J
target address
opcode
Branches and load/store are both I-format instructions; but branches use PC-relative addressing, whereas load/store use base addressing
Branches use PC-relative addressing; jumps use pseudo-direct addressing
Shifts use R-format, but other immediate instructions (addi, andi, ori) use I-format

## Slide 42
Summary (2/2)

## Slide 43: End of File